## Slide 1
TSC GTA 07-0001
MILES XXI GRAPHICS TRAINING AID (GTA)
for M2/M3A3
TRAINING SUPPORT CENTER

## Slide 2
Installation Checks
1. Ensure all cable connections are correct and secured.
2. Ensure proper placement of belts using Belt Amplifier Location. Front Amplifier is place above main gun mantle . The Right Amplifier is place center of turret on right side. The Left Amplifier is placed on top of TOW launcher on left side. The Rear Amplifier is placed lower center of bustle rack.
3. Ensure interior cables are routed thru center periscope between Commander and Gunners hatch.
4. Ensure all Velcro is properly secured to vehicle.
5. Ensure all cabling is properly routed and all excess cabling has been secured using zip-ties.

## Slide 3
Vehicle Setup Procedures
Vehicle Type
1. Turn on Vehicle Control Unit (VCU) power , a BIT test starts and system will go to a DEAD status. Use a Universal Controller Device (UCD) to RESET the vehicle.
2. The following menu will be displayed if system passes BIT WPN TYP MAIN GUN, M2 ALIVE
3. If vehicle type is not correct, use a UCD to put vehicle in CONTROL MODE by shooting any detector belt sensor. VDA will read ADMIN FUNCTIONS MENU
4. Scroll up or down till VDA states SELECT FOR CHOOSE VEHICLE TYPE then press SELECT and scroll to find M2 or M3 from displayed menu.
5. Once you find the vehicle press SELECT to
choose the vehicle then press SELECT again to
confirm vehicle type. VDA with beep confirming
selection. Scroll up to ADMIN FUNCTIONS to exit
then press SELECT to exit.

## Slide 4
Vehicle Setup Procedures
Fire Mode
1. Power on Vehicle Control Unit (VCU), a BIT test starts and system will go to a KILL status. Use the Universal Controller Device(UCD) to RESET the vehicle.
2. The following menu will be displayed if system passes BIT WPN TYP MAIN GUN, M2 ALIVE
3. Use a UCD to put vehicle in CONTROL MODE by shooting any detector belt sensor.
4. Observe on the Vehicle Display Assemble (VDA) it should read ADMIN FUNCTIONS MENU
5. Scroll up and down till VDA reads SELECT FOR CHOOSE FIRE MODE

## Slide 5
Vehicle Setup Procedures
Fire Mode ( Con’t)
6. Press SELECT and scroll to find appropriate
DRY FIRE MODE or BLANK FIRE MODE then
press SELECT.
7. The VDA will display SELECT CONFIRMS DRY
FIRE MODE or SELECT CONFIRMS BLANK FIRE
MODE then press SELECT.
8. Select INITIALIZE will be heard thru the intercom.
9. The VDA will display SELECT TO CHOOSE FIRE MODE
Scroll up till VDA displays ADMIN
FUNCTIONS SELECT TO EXIT press SELECT
11. VDA will display WPN TYP MAIN GUN, M2 ALIVE

## Slide 6
Loading Procedures
1. On VDA, scroll to WEAPON TYPE, press SELECT, then scroll till you find the Weapon that you want to load.
2. For MAIN GUN (25MM), Scroll to MAIN GUN, press SELECT, then scroll to AMMO TYPE, then press SELECT, then scroll to choose AP or HE, then press SELECT. After pressing SELECT for Ammo Type, VDA will go back to MAIN MENU.
3. Scroll to RELOAD MAIN GUN, then press SELECT.
4. Repeat steps 2 and 3 for what second Ammo Type
5. Repeat steps 2 and 3 for COAX.
6. Repeat steps 2 and 3 for TOW.

## Slide 7
Vehicle Display Assembly (VDA)Troubleshooting
M2A3/M3A3 MILES XXI
Problem: VDA has no display
1. Turn Vehicle Control Unit (VCU) off then back on. VDA runs BIT and goes into a KILLED status. Use UCD to RESET.
2. Is CVKI strobe light flashing?
A. YES – Is problem solved?
i. YES – Verify system is operational
ii. NO – Turn off VCU and replace System Cable. Does this solve the problem?
a. YES – Verify system is operational
b. NO – Turn off VCU then replace VDA, then turn on VCU. Does this solve your problem?
i. YES - Verify system is operational.
ii. NO – SEE MILES CONTACT TEAM
B. NO – SEE MILES CONTACT TEAM

## Slide 8
Vehicle Control Unit (VCU)Troubleshooting
M2A3/M3A3 MILES XXI
Problem: VCU will not power up.
1. Disconnect all cables from VCU. Power on VCU and within 30 seconds strobe light should blink.
A. If strobe light blinks replace Vehicle Control Interface (VCI). Then Retry.
B. If no blink strobe – SEE MILES CONTACT TEAM.
2. Ensure system cable is connected to vehicle power.
A. If not connected – connect and retry.
B. If connected – retry. If retry does not work – SEE MILES CONTACT TEAM

## Slide 9
1. Place vehicle on level platform with target placed at 1200 meters.
2. Ensure MILES XXI has been properly installed and configured for M2 or M3.
3. Turn on MILES XXI power.
4. Turn on vehicle Master Power then turn on turret power. NOTE: Ensure Commander’s Tactical Display reads TRAINING MODE NOT TACTICAL MODE.
5. Select alignment Aiming Point on designated target and lay gun manually on reticle aiming point.
6. Looking through the 12 power scope located inside the MGLT, unlock azimuth and elevation locking knobs. Using azimuth and elevation alignment screws, turn the alignment screws clockwise or counter clockwise to adjust the MGLT to the vehicles aim point. Lock down azimuth locking knob and then lock down elevation locking knob.
M2A3/M3A3 MILES XXI Boresight Procedures

## Slide 10
8. Select “BORESIGHT 25MM” from Commander’s Tactical Display (CTD).
9. Use Gunner’s Hand Station (GHS) to move reticle to aim point. Once aligned select “CALCULATE AND SAVE” on CTD.
10. Select “BORESIGHT 7.62” on CTD.
11. Move GHS to align sight to aim point. Once aligned select “CALCULATE AND SAVE” on CTD.
12. Select “BORESIGHT TOW” on CTD.
13. Move GHS to align sight to aim point. Once aligned select “CALCULATE AND SAVE” on CTD.
Align MGLT 12x reticle to the same aim
point.
15. Select all weapons and verify alignment of sights and MGLT. Then, fire at designated target with all weapons to confirm alignment.
M2A3/M3A3 MILES XXI Boresight Procedures

## Slide 11
MILES XXI |  | 
DIRECT FIRE KILL CODES |  | 
 |  | RANGE
CODE | WPN | MILES XXI
00 | Controller Gun | 300-500
01 | Hellfire | 8000
02 | N/A | 
03 | AT-3 | 1500
04 | N/A | 
05 | N/A | 
06 | N/A | 
07 | TOW | 3750
08 | Dragon | 1000
09 | F&F MSL | 4000
10 | 125MM | 3000
11 | M18 Claymore | 
12 | 105MM | 3000
13 | 122MM | 3000
14 | Rocket | 3000
15 | AT-4 | 300
16 | 120MM | 3750
17 | 90MM | 
18 | 152MM | Miles Only
19 | Grenade | 1500
20 | SMAW | 
21 | 30MM | 3000
22 | 25MM | 3000
23 | Vulcan | 1600
24 | Heavy Machine Gun (M2MG) | 1600
25 | Chaparral | 6000
26 | Stinger | 4000
27 | M16A1/A2, M60MG, M249, M240 | 160-800
28 | Heavy wpn Miss | 800
29 | Light Wpn Miss | 460
30 | Resurrection | 300-500
31 | Heavy SPR MS | 
33 | SA-14 | 
34 | ZSU 23-4 Radar Mode | 2800
36 | Reset | 300-500

## Slide 12
CATASTROPHIC PK FACTORS |  |  |  |  |  |  |  |  |  |  | 
M2/M3 VEHICLE |  |  |  |  |  |  |  |  |  |  | 
MILES | Front | R SIDE | REAR | L SIDE | SUB Pk FACTORS |  |  | AMMO FACTOR |  |  | 
Code | ZONE 1 | ZONE 2 | ZONE 3 | ZONE 4 | FpK | MobK | ComK | A | B | C | D
1 | 100 | 100 | 100 | 100 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
2 | 100 | 100 | 100 | 100 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
3 | 60 | 80 | 90 | 80 | 0.50 | 1.50 | 1.67 | 1.00 | 1.00 | 1.00 | 1.00
4 | 12 | 16 | 26 | 16 | 1.00 | 2.00 | 2.50 | 1.00 | 1.00 | 1.00 | 1.00
5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.02 | 100.00 | 0.02 | 1.00 | 1.00 | 1.00 | 1.00
6 | NE | NE | NE | NE |  |  |  |  |  |  | 
7 | 70 | 90 | 100 | 90 | 0.50 | 1.50 | 1.00 | 1.00 | 1.25 | 1.00 | 1.00
8 | 60 | 80 | 90 | 80 | 0.50 | 1.50 | 1.67 | 1.00 | 1.50 | 1.00 | 1.00
9 | 60 | 70 | 80 | 70 | 0.50 | 0.50 | 1.67 | 1.00 | 1.00 | 1.00 | 1.00
10 | 55 | 68 | 100 | 68 | 0.50 | 2.00 | 2.50 | 1.00 | 0.50 | 1.00 | 1.00
11 | NE | NE | NE | NE |  |  |  |  |  |  | 
12 | 26 | 33 | 44 | 33 | 0.50 | 2.00 | 2.50 | 1.00 | 0.50 | 1.00 | 1.00
13 | 23 | 29 | 38 | 29 | 0.50 | 2.00 | 2.50 | 1.00 | 0.50 | 1.00 | 1.00
14 | 2.5 | 5.5 | 8.5 | 5.5 | 1.00 | 2.00 | 10.00 | 1.00 | 2.00 | 1.00 | 1.00
15 | 21 | 26 | 33 | 26 | 0.50 | 1.00 | 1.67 | 1.00 | 2.00 | 1.00 | 1.00
16 | 26 | 33 | 44 | 33 | 0.50 | 2.00 | 2.50 | 1.00 | 0.50 | 1.00 | 1.00
17 | 23 | 29 | 38 | 29 | 0.50 | 2.00 | 3.00 | 1.00 | 0.50 | 1.00 | 1.00
18 | 23 | 29 | 38 | 29 | 0.50 | 2.00 | 3.00 | 1.00 | 1.00 | 1.00 | 1.00
19 | 0.5 | 1.5 | 2.5 | 1.5 | 0.50 | 1.00 | 8.00 | 1.00 | 1.00 | 1.00 | 1.00
20 | 10 | 15 | 20 | 15 | 1.00 | 2.50 | 10.00 | 1.00 | 1.00 | 1.00 | 1.00
21 | 5 | 10 | 15 | 10 | 2.00 | 2.00 | 10.00 | 1.00 | 1.00 | 1.00 | 1.00
22 | 10 | 15 | 20 | 15 | 1.00 | 1.00 | 2.00 | 1.00 | 0.50 | 1.00 | 1.00
23 | 5 | 10 | 15 | 10 | 0.02 | 1.00 | 2.00 | 1.00 | 0.50 | 1.00 | 1.00
24 | 0.5 | 0.5 | 1 | 0.5 | 0.02 | 0.02 | 5.00 | 1.00 | 1.00 | 1.00 | 1.00
25 | NE | NE | NE | NE |  |  |  |  |  |  | 
26 | NE | NE | NE | NE |  |  |  |  |  |  | 
27 | NE | NE | NE | NE |  |  |  |  |  |  | 
28 | NM | NM | NM | NM |  |  |  |  |  |  | 
29 | NE | NE | NE | NE |  |  |  |  |  |  | 
30 | OP | OP | OP | OP |  |  |  |  |  |  | 
31 | NM | NM | NM | NM |  |  |  |  |  |  | 
32 | NE | NE | NE | NE |  |  |  |  |  |  | 
33 | NE | NE | NE | NE |  |  |  |  |  |  | 
34 | NE | NE | NE | NE |  |  |  |  |  |  |