## Slide 1
TSC GTA 17-0002
MILES XXI GRAPHICS TRAINING AID (GTA)
for M1A2 SEP TANK
TRAINING SUPPORT CENTER

## Slide 2
Installation Checks
1. Ensure all cable connections are correct and secured.
2. Ensure proper placement of belts using Belt Amplifier Location. Front Amplifier is place above main gun mantle . The Right Amplifier is place center of turret on right side. The Left Amplifier is placed center left side of turret. The Rear Amplifier is placed lower center of bustle rack.
3. Ensure Velcro is place on Loaders Hatch and Loaders Hatch periscope is turned 180o to face the rear of the vehicle.
4. Ensure all Velcro is properly secured to vehicle.
5. Ensure all cabling is properly routed and all excess cabling has been secured using zip-ties.

## Slide 3
Vehicle Setup Procedures
Vehicle Type
1. Turn on Vehicle Control Unit (VCU) power , a BIT test starts and system will go to a DEAD status. Use a Universal Controller Device (UCD) to RESET the vehicle.
2. The following menu will be displayed if system passes BIT WPN TYP MAIN GUN, M1 ALIVE
3. If vehicle type is not correct, use a UCD to put vehicle in CONTROL MODE by shooting any detector belt sensor. VDA will read ADMIN FUNCTIONS MENU
4. Scroll up or down till VDA states SELECT FOR CHOOSE VEHICLE TYPE then press SELECT and scroll to find M1 from displayed menu.
5. Once you find the vehicle press SELECT to
choose the vehicle then press SELECT again to
confirm vehicle type. VDA with beep confirming
selection. Scroll up to ADMIN FUNCTIONS to exit
then press SELECT to exit.

## Slide 4
Loading Procedures
1. On VDA, scroll to RELOAD MAIN GUN, press SELECT. This will load 1 round. It will take 5 seconds to reload.
2. For MAIN GUN, scroll to MAIN GUN, press SELECT, then scroll to AMMO TYPE, then press SELECT, then scroll to choose SABOT or HEAT, then press SELECT. After pressing SELECT for Ammo Type, VDA will go back to MAIN MENU.
3. Scroll to RELOAD MAIN GUN, then press SELECT.
4. Repeat steps 2 and 3 for what second Ammo Type
5. Loader must repeat step 1 after each round is fired.
6. Repeat steps 2 and 3 for COAX.
NOTE: Ammo loaded must match what Gunner has selected.

## Slide 5
Vehicle Display Assembly (VDA)Troubleshooting
M1A2 SEP MILES XXI
Problem: VDA has no display
1. Turn Vehicle Control Unit (VCU) off then back on. VDA runs BIT and goes into a KILLED status. Use UCD to RESET.
2. Is CVKI strobe light flashing?
A. YES – Is problem solved?
i. YES – Verify system is operational
ii. NO – Turn off VCU and replace System Cable. Does this solve the problem?
a. YES – Verify system is operational
b. NO – Turn off VCU then replace VDA, then turn on VCU. Does this solve your problem?
i. YES - Verify system is operational.
ii. NO – SEE MILES CONTACT TEAM
B. NO – SEE MILES CONTACT TEAM

## Slide 6
Vehicle Control Unit (VCU)Troubleshooting
M1A2 SEP MILES XXI
Problem: VCU will not power up.
1. Disconnect all cables from VCU. Power on VCU and within 30 seconds strobe light should blink.
A. If strobe light blinks replace Vehicle Control Interface (VCI). Then Retry.
B. If no blink strobe – SEE MILES CONTACT TEAM.
2. Ensure system cable is connected to vehicle power.
A. If not connected – connect and retry.
B. If connected – retry. If retry does not work – SEE MILES CONTACT TEAM

## Slide 7
M1A2 SEP MILES XXI Boresight Procedures
1. Position Tank on level ground with the main
gun over front slope.
2. Ensure MILES XXI has been properly
installed and configured to M1.
3. Set a MILES equipped target at max allowable
distance based on terrain.
4. Turn the Tank Master Power on.
Turn Turret Power on.
6. On the CITV “SELECT” PRE POST.
7. Then “SELECT” AUX SYSTEMS.
8. Then “SELECT “ AUX CONTROLS.
9. Then “PRESS” TUR UTIL button to turn ON.
10. With the Engine Running, the Hydraulic
Pressure Gage should read between 1500-1700
PSI. (Engine not running you must turn on AUX
pump).
11. Set Thermal Mode to Stand-By.
12. Set Main Gun switch to Main Gun, and Air /
Ground switch to Ground, High Mag and index
SABOT.
13. Push SENSORS, Push LEAD, Push MANUAL,
Enter 0.00, Push Enter, Return 1X .
14. Push ATTD, Push PITCH/ROLL, Push OFF,
Push CANT, Push MANUAL, Index 0.00, push
Enter, Return 3X.

## Slide 8
M1A2 SEP MILES XXI Boresight Procedures
15. Push METRL DATA, Push CROSSWIND, Push
MANUAL, Index 00.00, Push Enter Return 2X.
16. Push SENSORS, Push Range, INDEX RANGE,
Push Enter, Return 2X.
17. Push ADJUST, Push AMMO SUBDES, Use the
arrow key to select MILES SUBDES,
18. Push Enter, Return 2X.
19. Push ADJUST, Push ZERO, and enter 0.00
PUSH ENTER, 0.00 PUSH ENTER, Return 2X.
20. Push ADJUST, Push BORESIGHT, Press GPS,
Enter 0.00 PUSH ENTER, 0.00 PUSH ENTER,
Return 3X.
21. Squeeze the Power Control Handles for 3
seconds to input all Data.
22. Look through the GPS reticle and lay the Gun
center mass of the boresight target
Look through the MGLT Scope and lay the
MGLT crosshairs center mass of the boresight
target.
24. Boresighting is now Completed.
25. With the GPS reticle center mass, fire the
main gun, if the light flashes (4 times) the Gun is
“Zeroed”.

## Slide 9
MILES XXI |  | 
DIRECT FIRE KILL CODES |  | 
 |  | RANGE
CODE | WPN | MILES XXI
00 | Controller Gun | 300-500
01 | Hellfire | 8000
02 | N/A | 
03 | AT-3 | 1500
04 | N/A | 
05 | N/A | 
06 | N/A | 
07 | TOW | 3750
08 | Dragon | 1000
09 | F&F MSL | 4000
10 | 125MM | 3000
11 | M18 Claymore | 
12 | 105MM | 3000
13 | 122MM | 3000
14 | Rocket | 3000
15 | AT-4 | 300
16 | 120MM | 3750
17 | 90MM | 
18 | 152MM | Miles Only
19 | Grenade | 1500
20 | SMAW | 
21 | 30MM | 3000
22 | 25MM | 3000
23 | Vulcan | 1600
24 | Heavy Machine Gun (M2MG) | 1600
25 | Chaparral | 6000
26 | Stinger | 4000
27 | M16A1/A2, M60MG, M249, M240 | 160-800
28 | Heavy wpn Miss | 800
29 | Light Wpn Miss | 460
30 | Resurrection | 300-500
31 | Heavy SPR MS | 
33 | SA-14 | 
34 | ZSU 23-4 Radar Mode | 2800
36 | Reset | 300-500

## Slide 10
CATASTROPHIC PK FACTORS |  |  |  |  |  |  |  |  |  |  | 
M1 TANK - 120mm |  |  |  |  |  |  |  |  |  |  | 
MILES | Front | R SIDE | REAR | L SIDE | SUB Pk FACTORS |  |  | AMMO FACTOR |  |  | 
Code | ZONE 1 | ZONE 2 | ZONE 3 | ZONE 4 | FpK | MobK | ComK | A | B | C | D
1 | 100 | 100 | 100 | 100 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
2 | 60 | 90 | 100 | 90 | 0.80 | 1.25 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
3 | 10 | 40 | 90 | 40 | 0.80 | 2.00 | 10.00 | 1.00 | 1.00 | 1.00 | 1.00
4 | 0.5 | 0.5 | 2.5 | 0.5 | 1.00 | 4.00 | 20.00 | 1.00 | 1.00 | 1.00 | 1.00
5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.02 | 200.00 | 0.02 | 1.00 | 1.00 | 1.00 | 1.00
6 | NE | NE | NE | NE |  |  |  |  |  |  | 
7 | 25 | 35 | 30 | 35 | 1.50 | 2.00 | 2.25 | 1.00 | 1.25 | 1.00 | 1.00
8 | 2 | 10 | 30 | 10 | 1.00 | 5.00 | 50.00 | 1.00 | 1.50 | 1.00 | 1.00
9 | 50 | 70 | 90 | 70 | 0.10 | 0.50 | 2.00 | 1.00 | 1.00 | 1.00 | 1.00
10 | 5 | 10.5 | 16.5 | 10.5 | 2.50 | 3.00 | 5.00 | 1.00 | 0.50 | 1.00 | 1.00
11 | NE | NE | NE | NE |  |  |  |  |  |  | 
12 | 7 | 10 | 12 | 10 | 1.50 | 1.75 | 3.00 | 1.00 | 0.50 | 1.00 | 1.00
13 | 0.5 | 1.5 | 2.5 | 1.5 | 1.00 | 4.00 | 10.00 | 1.00 | 0.50 | 1.00 | 1.00
14 | 0.5 | 2.5 | 8.5 | 2.5 | 1.00 | 3.00 | 10.00 | 1.00 | 2.00 | 1.00 | 1.00
15 | 0.5 | 1.5 | 5.5 | 1.5 | 1.00 | 4.00 | 8.00 | 1.00 | 2.00 | 1.00 | 1.00
16 | 8.5 | 12 | 14 | 12 | 1.50 | 1.75 | 3.00 | 1.00 | 0.50 | 1.00 | 1.00
17 | 0.5 | 2.5 | 8.5 | 2.5 | 1.00 | 4.00 | 8.00 | 1.00 | 0.50 | 1.00 | 1.00
18 | 0.5 | 1.5 | 2.5 | 1.5 | 1.00 | 4.00 | 10.00 | 1.00 | 1.00 | 1.00 | 1.00
19 | 0.5 | 0.5 | 0.5 | 0.5 | 0.02 | 0.50 | 5.00 | 1.00 | 1.00 | 1.00 | 1.00
20 | 1 | 10 | 40 | 10 | 1.00 | 3.00 | 10.00 | 1.00 | 1.00 | 1.00 | 1.00
21 | 1 | 3 | 15 | 3 | 10.00 | 5.00 | 33.30 | 1.00 | 1.00 | 1.00 | 1.00
22 | 0.5 | 0.5 | 1 | 0.5 | 0.02 | 0.50 | 5.00 | 1.00 | 0.50 | 1.00 | 1.00
23 | 0.5 | 0.5 | 1 | 0.5 | 0.02 | 0.50 | 5.00 | 1.00 | 0.50 | 1.00 | 1.00
24 | 0.5 | 0.5 | 0.5 | 0.5 | 0.02 | 0.02 | 4.00 | 1.00 | 1.00 | 1.00 | 1.00
25 | NE | NE | NE | NE |  |  |  |  |  |  | 
26 | NE | NE | NE | NE |  |  |  |  |  |  | 
27 | NE | NE | NE | NE |  |  |  |  |  |  | 
28 | NM | NM | NM | NM |  |  |  |  |  |  | 
29 | NE | NE | NE | NE |  |  |  |  |  |  | 
30 | OP | OP | OP | OP |  |  |  |  |  |  | 
31 | NM | NM | NM | NM |  |  |  |  |  |  | 
32 | NE | NE | NE | NE |  |  |  |  |  |  | 
33 | NE | NE | NE | NE |  |  |  |  |  |  | 
34 | NE | NE | NE | NE |  |  |  |  |  |  |